| Roadside Safety Pooled Fund Program Problem Statement/Research Proposal | State: Louisiana 2015 – LA-104 |
| --- | --- |
| Title: Retest of Temporary Precast Barrier (Freestanding and Anchored to Concrete Pavement) for MASH, Test Level 3 |
| Problem Statement: Through this Pooled Fund Group, Louisiana has developed a Temporary Precast Concrete Barrier system that can be anchored in concrete and asphalt pavements. The basic, freestanding barrier was based on an Oregon DOT detail that was developed under NCHRP 350. A previous pooled fund project (405160-3) adapted this detail and developed a method to anchor the barrier into concrete pavement. This anchored detail was also developed using NCHRP 350. All subsequent tests on this temporary barrier system have used the MASH criteria. Louisiana would like to retest the freestanding and anchored in concrete conditions for MASH so as to have a complete system with all aspects tested and approved under the same criteria. |
| Objectives of the Study: This proposal would perform an analysis of the existing freestanding and anchored in concrete details to determine if it can be accepted as a MASH Test Level 3 system. If the analysis is inconclusive, a full scale crash test would be performed. |
| Expected Benefits: This proposal would result in a temporary precast barrier system with all details and applications approved under the MASH criteria. |
| Description of the Proposed Feature to be Tested: (Be as detailed as possible. Include drawings and/or plans, if available.) A detail of the proposed barrier has been attached. LADOTD can provide barrier segments for testing if necessary. |
| Estimated Cost (of the feature per linear foot installed): | Total Estimated Cost of Crash Test: |
| Contact Person: Kurt Brauner | Telephone: 225-379-1933 |