## Slide 1: Roadside Safety Pooled Fund Program Research Update
Roger Bligh, Ph.D., P.E.
Senior Engineer
TTI - Roadside Safety & Physical Security Division
Ph.: 979-845-4377
E-Mail: R-Bligh@tti.tamu.edu
Roadside Safety Pooled Fund Program – Fall Meeting 2018
Denver, Colorado
September 18th 2018

## Slide 2: Additional Projects
Analysis and Testing of Florida Department of Transportation Barrier Systems for MASH Compliance
MASH Implementation Support for WSDOT
W-beam Guardrail Evaluation with Posts in Sleeves
MASH Testing of Massachusetts S3-MTL4 Curb Mounted & Back of Sidewalk Mounted Bridge Railings
MASH Testing of Transition from Weak Post MGS System to Strong Post MGS System
MASH Testing and Evaluation of the Merritt Parkway Guiderail

## Slide 3: Analysis and Testing of Florida Department of Transportation Barrier Systems for MASH Compliance
TTI Researcher: James Kovar
Technical Representative: Derwood Sheppard (FDOT)

## Slide 4: Analysis and Testing of Florida DOT Barrier Systems for MASH Compliance
Task 1: MASH Testing of Special Baseplate Posts
  Subtask 1.1: Analysis and Design of Guardrail Posts on Concrete Structures Detail
  Subtask 1.2: Pendulum Testing of Two Post Designs
  Subtask 1.3: MASH Testing of Final Post Design (MASH Test 2-11)
Task 2: MASH 4-11 Testing of Combination Traffic-Pedestrian-Bicycle Bridge Railing
  Subtask 2.1 – System Construction
  Subtask 2.2 – Full-Scale Crash Test and Report (MASH Test 3-11)
Task 3: MASH Testing of W-Beam Median Guardrail w/ Rub Rail
  Subtask 3.1: Construction and Demolition
  Subtask 3.2: Crash Testing and Reporting (MASH Tests 3-11 and 3-10)

## Slide 5: MASH Implementation Support for WSDOT
TTI Researcher: Nauman Sheikh
Technical Representative: Jeff Petterson (WSDOT)

## Slide 6: MASH Implementation Support for WSDOT
Need
  WSDOT needs assessment of various safety hardware to determine which systems may need testing, and/or formal engineering opinions for MASH compliance
Objective
  Based on past testing and literature review, TTI is to assess systems prioritized by WSDOT and report whether they are likely to be MASH compliant, and if not, what tests or analyses may be needed

## Slide 7: MASH Implementation Support for WSDOT
Progress
  Three systems were prioritized in the first round
  TTI has provided assessment on one of the three
    Embedded single slope barrier with drainage scuppers
Future Tasks
  TTI to provide assessment on remaining two systems
  A new list of revised systems will be provided by WSDOT for further assessment by TTI

## Slide 8: W-beam Guardrail Evaluation with Posts in Sleeves
TTI Researcher: Nauman Sheikh
Technical Representative: Carolyn Morehouse (AKDOT)

## Slide 9: W-beam Guardrail Posts in Sleeves
Need
  Due to frozen soil, guardrail and terminal posts are sometimes installed in steel tubes (sleeve)
  It is not know if this practice alters the performance of the guardrail to be MASH compliant
Objective
  Perform a series of bogie testing with posts installed in standard soil and in sleeve to compare post reponse
  Perform a full-scale MASH crash test on a generic system with posts installed in sleeve

## Slide 10: W-beam Guardrail Posts in Sleeves
Progress
  Project was on hold due to funding issues
  Notice to proceed received Sep. 13, 2018
  Work will commence shortly
Future Tasks
  Work will commence shortly

## Slide 11: MASH Testing of Massachusetts S3-MTL4 Curb Mounted & Back of Sidewalk Mounted Bridge Railings
TTI Researcher: Chiara S. Dobrovolny
Technical Representative: Alex Bardow (MassDOT)

## Slide 12: MASH Testing of MassDOT S3-MTL4 Curb Mounted & Back of Sidewalk Mounted Bridge Railings
MASH Testing of Massachusetts S3-MTL4 Curb Mounted Railing
  Full Matrix MASH TL-4

## Slide 13: MASH Testing of MassDOT S3-MTL4 Curb Mounted & Back of Sidewalk Mounted Bridge Railings
MASH Testing of Massachusetts S3-MTL4 Back of Sidewalk Mounted Railing
  Full Matrix MASH TL-4

## Slide 14: MASH Testing of Transition from Weak Post MGS System to Strong Post MGS System
TTI Researcher: Chiara S. Dobrovolny
Technical Representative: David Kilpatrick (CTDOT)

## Slide 15: MASH Testing of Transition from Weak Post MGS to Strong Post MGS
  Full Scale MASH Tests 3-21 and 3-20 on Downstream End of Weak to Strong Transition

## Slide 16: MASH Testing and Evaluation of the Merritt Parkway Guiderail
TTI Researcher: Chiara S. Dobrovolny
Technical Representative: David Kilpatrick (CTDOT)

## Slide 17: MASH Testing and Evaluation of the Merritt Parkway Guiderail
  Planned full scale MASH tests:
  Test 3-11 & 3-10 on LON, no Curb
  Test 3-11 & 3-10 on LON, With Curb
  Test 3-21 & 3-20 on Transition to Concrete Parapet