## Slide 1: Design and Testing of a MASH TL-3 Thrie-Beam System for Roadside and Median Applications
PS Developers
Jim (MassDOT), Joe (WVDOT), Kurt (LADOTD), Filiberto (IDOT)
Project Synopsis
  Develop and crash test a MASH TL-3 thrie-beam roadside and a median system
  Develop transition from w-beam to thrie-beam through computer simulation
Project Goal(s)
  Develop designs for a MASH TL-3 thrie-beam roadside system and a median system
  MASH crash test the newly developed thrie-beam designs
  Develop transition from w-beam to thrie-beam through computer simulation
2019-13-LSRB

## Slide 2
Project Background
  G9 thrie-beam failed MASH testing
  Need also exists for a transition and termination method
  Crash testing for the transition will be balloted for prioritization next year because of budgetary concerns
  Development of termination method will be balloted for prioritization next year because of budgetary concerns
Proposed Work Plan
  Task 1: Literature and Engineering Review
    Review previous literature and research
    Preliminary analysis preparing for simulation
  Task 2: Computer Modeling and Simulation
    Develop roadside, median, and transition systems
  Task 3: MASH Crash Testing
    Crash test the roadside and median systems to MASH TL-3.
  Task 4: Reporting
    Complete the final technical report documenting all of the work completed in this project.
2019-13-LSRB
Design and Testing of a MASH TL-3 Thrie-Beam System for Roadside and Median Applications

## Slide 3
Deliverables
  MASH TL-3 crash tested designs for roadside and median thrie-beam barriers
  Computer simulated design for a transition from w-beam to thrie-beam guardrail
  Technical report documenting the project
Urgency and Expected Benefit
  Limited available guardrail options for enhanced protection from hazards
  Immediate benefit to safety by reducing impact severity and financially by having an alternative to concrete barrier.
Funding
  $300,000
Research Period
  18 months
2019-13-LSRB
Design and Testing of a MASH TL-3 Thrie-Beam System for Roadside and Median Applications

## Slide 4: 31” Rectangular Wood Post W-Beam Guardrail in Concrete Mow Strips
PS Developers Kurt Brauner, LA
Project Synopsis
  Design wood-post guardrail installed in concrete mow strip with leave outs around posts that are backfilled with weaker material to allow the post to deflect on MASH TL-3 impacts
Project Goal(s)
Develop and analyze various options that will allow a wood post used in a concrete mow strip to perform properly when used as part of MASH TL-3 guardrail
2019-15-LSRB
Project Background
  TTI performed MASH testing with wood-post mow-strip
    Small car Test 3-10 passed with 40 inch post embedment
    Pickup truck Test 3-11 failed with 40 inch embedment
    Pickup truck Test 3-11 failed with 36 inch post embedment
  Previous research by TTI under NCHRP Rep. 350 may be useful for this project.

## Slide 5: 31” Rectangular Wood Post W-Beam Guardrail in Concrete Mow Strips
Proposed Work Plan
Task 1: Design
  Evaluate past testing to develop design changes with likelihood of success
  Use past testing as guidance for the design changes
Task 2: Construction, Testing, & Reporting
  Construct guardrail for testing
  Perform MASH Test 3-11
    It is expected that that Test 3-10 would not be needed due to changes being small and the previous successful Test 3-10 with 40-inch post embedment
  Final Report
Deliverables
Final report
Engineering drawings
2019-15-LSRB

## Slide 6: 31” Rectangular Wood Post W-Beam Guardrail in Concrete Mow Strips
Urgency and Expected Benefit
Wood post guardrail is widely used in mow-strips based on past successful performance under NCHRP Report 350
Having a MASH approved system is essential and will have immediate implementation
Funding
Task 1 – Redesign $5,000
Task 2 – Construction, Testing, & Reporting $55,000
TOTAL $60,000
Research Period
6 months
2019-15-LSRB

## Slide 7: BIB Terminal Variations in Foreslope/Backslope/Ditch Configurations
PS Developers: Jeff (AK); Christopher (OR), Josh (CO), Fil (IL)
Project Synopsis
  Evaluate range of BIB ditch configurations (site variations from crash tested conditions), producing acceptable results under MASH conditions.
Project Goal(s)
Consider variations from crash tested configuration to establish:
• BIB terminal may be installed on foreslope flatter than 4:1;
• Flattest effective backslope; investigate whether there is a limit for backslope steepness;
• BIB terminal may be installed in flat-bottomed ditches;
• Design alterations from previous tested configuration, if any, when ditch configurations vary
2019-17-LSRB
Project Background
  MASH crash test: 4:1 Foreslope/ 2:1 Backslope/ V-Ditch, TTI project 608431, tests 3-34, 3-35
Notes: Flattest effective backslope; a threshold backslope for requiring area free of fixed objects behind the terminal; and investigate whether there is a limit for backslope steepness.
Ditch configurations vary: the foreslope is flatter than 4:1; foreslope of the ditch is wider than 6 feet; the backslope varies from 2:1; or the ditch is flat-bottomed

## Slide 8
Proposed Work Plan
Task 1. DOT Members Survey.
Identify common applicable ranges with respect to research parameters in use (and needed) by DOT Members (degree of backslope, type of ditch configuration, ditch width, rubrail /no rubrail)
Task 2. Engineering Analysis and Finite Element Investigation.
Conduct engineering analysis to identify most critical cases based on Task 1 results.
Conduct FE computer simulations to investigate critical cases for system crashworthiness.
Task 3. Recommendations.
Summarize recommendations based on engineering analysis (and FEA).
Deliverables
Acceptable limits for foreslope (flatter than 4:1), and backslope (range of variation from 2:1 and critical slope), offset to ditch bottom or width of foreslope, and width of flat-bottomed ditch.
Necessary changes to design for variations
BIB Terminal Variations in Foreslope/Backslope/Ditch Configurations
2019-17-LSRB

## Slide 9: BIB Terminal Variations in Foreslope/Backslope/Ditch Configurations
Urgency and Expected Benefit
MASH tests successfully completed (3-34, 3-35) for one site configuration. States have variable design standards for ditches and adapting the device for site variability would increase the number of locations this device could be installed.
BIB Terminal eliminates potential for terminal end strike. Because of the slopes involved, other issues need to be considered. If acceptable limits for site variability can be shown, wider installation may reduce risk to the traveling public.
Funding: $90,000
Research Period : 1 year
2019-17-LSRB

## Slide 10: MASH TL-2 Evaluation and MASH determination of 8-inch vertical curb with MGS traffic barrier
PS Developers
Project Synopsis
  Evaluate and potentially crash test a 8-inch tall vertical curb with MGS traffic barrier in accordance with MASH Test Level 2 (TL-2)
Project Goal(s)
To evaluate 8-inch vertical curb flush with MGS traffic barrier that is MASH TL-2 compliant
2019-18-LSRB
Project Background
MDOT uses combination of curb and MGS guardrail with face of barrier rail flush with face of the curb + MGS guardrail with curb and sidewalk has barrier offset from curb (MD 605.31)
PennDOT uses 8 in. curb for roadways and 4 in. curb is used with traffic barrier. 4 in. curb often cannot be used on projects, and then 8 in. curb is allowed with stiffened traffic barrier(PennDOT Guide rail with curb detail)
MDOT
PennDOT

## Slide 11: MASH TL-2 Evaluation and MASH determination of 8-inch vertical curb with MGS traffic barrier
2019-18-LSRB
Project Background
Type A – 8 inch
Type B – 6 inch
Type C – 3 inch
Type D – 6 inch

## Slide 12: MASH TL-2 Evaluation and MASH determination of 8-inch vertical curb with MGS traffic barrier
2019-18-LSRB
Project Background
Standard is 8-inch vertical curb
Most existing curbs are 8-inches
Guiderail often installed at existing curbs
Standard inlet is 8-inch high
Curbed sections need inlets

## Slide 13: MASH TL-2 Evaluation and MASH determination of 8-inch vertical curb with MGS traffic barrier
2019-18-LSRB
Project Background
This often cannot be done on projects because:
The existing curb is 8-inch
8-inch curb needed for drainage and inlets
Then 8-inch curb is allowed with stiffened guardrail, i.e., close post spacing, which can cause conflicts with inlet boxes.
Curb flush with w-beam

## Slide 14: MASH TL-2 Evaluation and MASH determination of 8-inch vertical curb with MGS traffic barrier
2019-18-LSRB
Project Background
Note: 8-inch curb is sometimes used

## Slide 15
Proposed Work Plan
Build a confidence level (validation) of the simulation model of the guardrail with a curb by simulating MASH tested designs (e.g. ones conducted at the MwRSF)
Evaluate MGS traffic barrier installed along a 8-inch curb using LS-DYNA simulation for MASH TL-2 criteria
Evaluate and determined acceptable offset from face of curb, if barrier is pushed back
Identify the most critical successful configuration based on the simulation
Evaluate and perform MASH compliance via crash testing
Deliverables
Details of traffic barrier face flushed with face of 8-inch curb
Variation of barrier offset from curb documentation of the evaluation
Crash tests results and the assessment of the performance according to MASH Test Level 2 (or TL-2) specifications
Engineering opinion for MASH compliance for similar, less critical, designs
2019-18-LSRB
MASH TL-2 Evaluation and MASH determination of 8-inch vertical curb with MGS traffic barrier

## Slide 16: MASH TL-3 Thrie-Beam transition from 31" W-Beam guardrail to single slope CIP concrete barrier
PS Developers
Nina Ertel, P.E, PennDOT.; Joe Hall, WVDOT
Project Synopsis
  Evaluate MASH TL-3 compliance of a Thrie-Beam transition from 31" W-Beam guardrail to single slope CIP concrete barriers.
Project Goal(s)
  Determine MASH TL-3 compliance of a Thrie-Beam transition from 31" W-Beam guardrail to single slope CIP concrete barrier either with engineering opinion or crash testing.
Project Background
  31” guiderail to F-shape and single slope CIP concrete barrier transition along the side of the road is a very common application.
  There is already a MASH compliant thrie-beam to F-shape bridge barrier. However, the end of the bridge is modified where the thrie-beam connects.
  Can this MASH compliant thrie beam transition be modified to connect to a F-shape for various heights and 42” high single slope CIP barrier without modifying the end?
2019-19-LSRB

## Slide 17: MASH TL-3 Thrie-Beam transition from 31" W-Beam guardrail to single slope CIP concrete barrier
Proposed Work Plan
Task 1: Literature Review and Engineering Analysis
  Evaluate current TL-3 Thrie-beam transition designs
  Determine the critical transition design and evaluate the transition for TL-3 compliance
  Evaluate and perform MASH compliance via engineering opinion, simulation and/or crash testing
Task 2: Construction and Demolition
Task 3: Full-Scale Crash Testing and Reporting
  Perform critical full-scale crash tests (budgeting for two crash tests)
  Provide a final report summarizing the details of the test installation, final drawings, and our finding and conclusions
  Provide engineering opinion on any acceptable variations
Deliverables
A report providing an evaluation of MASH TL-3 compliance of a Thrie-Beam transition from 31" W-Beam guardrail to single slope CIP concrete barrier. Include engineering opinion for MASH compliance for similar, less critical designs from various states which were not crash tested.
2019-19-LSRB

## Slide 18: MASH TL-3 Thrie-Beam transition from 31" W-Beam guardrail to single slope CIP concrete barrier
Urgency and Expected Benefit
Transitions between w-beam and CIP concrete barriers is a common application.
As new MASH compliant barriers are being adopted by DOT’s, new transitions are needed in order to implement the new concrete barriers for use.
Funding
Total Estimated Cost = $140,000
Note: Budgeting for two full-scale crash tests on either single slope or F-shape.
Research Period
Work Schedule: (Project Duration = 10 months from initiation of the project)
Task 1 = 3 months
Task 2 = 3 months
Task 3 = 4 months
2019-19-LSRB

## Slide 19: Determination of the Length-of-Need for Guardrail without Anchorage Phase 2: MASH Crash Testing
PS Developers
Joe (WVDOT)
Project Synopsis
  Continuation of Phase 1
  Evaluate the length-of-need for guardrail without anchorage through crash testing
Project Goal(s)
  Evaluate the unanchored guardrail system developed in Phase 1 through full-scale MASH crash testing
Project Background
  Phase 1 prioritized in FY19
  Phase 1 determines the LON through computer simulation
  Phase 1 completes component testing to validate computer models
  Phase 2 completed project with MASH crash testing
2019-20-LSRB

## Slide 20
Proposed Work Plan
  Task 1: MASH Crash Testing
    Crash test the guardrail system to MASH TL-3.
Deliverables
  Minimum required length-of-need for a guardrail system without anchorage
  Technical report documenting all of the work completed in this project
Urgency and Expected Benefit
  Guidance is needed for safely installing guardrail systems before anchorage is installed
  States will be able to safely protect errant motorists under this unanchored condition
Funding
  $130,000
Research Period
  9 months
2019-20-LSRB
Design and Testing of a MASH TL-3 Thrie-Beam System for Roadside and Median Applications

## Slide 21: Steel Post Downstream End Anchor
PS Developers: Jeff (AK)
Project Synopsis
  Evaluate design alternatives for Steel Post Downstream End Anchor for 31” w-beam guardrail and conduct crash testing under MASH 2016 conditions. Project will use analysis, simulation, as required, and conduct full-scale testing necessary to obtain an eligibility letter.
Project Goal(s)
Design and test a steel post downstream end anchor as an alternative to existing MASH 2016 compliant w-beam guardrail end anchors that use timber posts.
2019-36-LSRB
Project Background
  Wood anchor posts have failed in testing. Need for material w/ consistent and reliable material properties.
  BCT Timber posts in BCT Post Sleeves: maintenance issues.
  Alternative: steel posts easier to maintain (?), more dependable than wood posts (?)
  Steel posts (direct bury or in tubes)  easier replacement /maintenance, durability

## Slide 22
Proposed Work Plan
Task 1. Design Development & Finite Element Investigation.
Develop design system
Conduct finite element simulation as design aid and to investigate CIP for full-scale crash testing.
Task 2. Component Testing.
Develop appropriate component testing as design aid for the proposed system, and as preliminary component behavior investigation.
Task 3. System Construction & Full-Scale Crash Testing.
Build test article.
Conduct full-scale crash testing.
Deliverables
Provide a downstream end anchor design that relies on steel posts. Provide a crash test report and supporting materials sufficient for FHWA consideration of a MASH eligibility letter.
Steel Post Downstream End Anchor
2019-36-LSRB

## Slide 23: Steel Post Downstream End Anchor
Urgency and Expected Benefit
Failure of BCT timber posts in downstream end anchors suggests an alternative should be investigated. Maintaining tension in a w-beam barrier system is critical to guardrail performance and reducing road user risk to an acceptable level.
Improving ease of maintenance can reduce exposure of motorists to temporary work zones and equipment, and shorten the time maintenance personnel are exposed to traffic when working near open lanes of traffic.
Steel posts are less prone to rot, pests, or undetected structural weakness or damage than wood posts. Reducing use of wood posts where possible may provide immediate safety and service advantages.
Funding: $170,000
Research Period : 18 months
2019-36-LSRB

## Slide 24: BIB Terminal Additional Crash Testing
PS Developers: Jeff (AK); Christopher (OR), Josh (CO), Fil (IL)
Project Synopsis
  Conduct additional crash testing as required by FHWA, producing acceptable results under MASH conditions to qualify for an FHWA eligibility letter.
  Project will use analysis, simulation, as required, and conduct required testing
Project Goal(s)
Conduct additional crash testing required by revision to MASH16. Additional crash testing is TBD.
Tests 3-34 and 3-35 were conducted successfully with the following BIB configuration: 4:1 Foreslope/ 2:1 Backslope/ V-Ditch.
2019-37-LSRB
Project Background
  MASH 2016 crash tests 3-34 (car) and 3-35 (pickup) conducted successfully on 4:1 Foreslope/ 2:1 Backslope/ V-Ditch. Other tests identified in MASH16 were evaluated as “non-relevant” and were not conducted

## Slide 25
Proposed Work Plan
Task 1. Finite Element Investigation on the Newly Proposed Tests.
Conduct finite element simulation to investigate CIP for additional full-scale crash testing.
Task 2. System Construction & Full-Scale Crash Testing.
Build test article.
Conduct additional full-scale crash testing.
Task 3. Recommendations.
Summarize recommendations based on additional testing.
Deliverables
Crash test results (tests TBD) and supporting materials which, when presented in combination with the results and materials obtained under Test Report Number 608431-07-1&2, will be sufficient to request FHWA consideration for an eligibility letter.
BIB Terminal Additional Crash Testing
2019-37-LSRB

## Slide 26: BIB Terminal Additional Crash Testing
Urgency and Expected Benefit
MASH tests have been successfully completed (3-34, 3-35) which show that small cars do not snag with an elevated rail height and the system has strength to withstand pickup truck impact. At a future time, FHWA may require additional crash testing in order to issue an eligibility letter for installation on the NHS.
BIB Terminal eliminates the potential for terminal end strike. Completing additional testing required in order to obtain an FHWA eligibility letter will enable wider installation of this terminal across the NHS with the potential to reduce risk to the traveling public.
Funding: $100,000
Research Period : 1 year
2019-37-LSRB

## Slide 27: Design and Testing of a Thrie-beam System at a Fixed Object
PS Developers
John (WSDOT)
Project Synopsis
  Develop and crash test a MASH TL-3 thrie-beam roadside system at a fixed object
  System to have minimal deflection and “close to rigid” behavior
  Cost effective alternative to concrete barrer
Project Goal(s)
  Develop and crash test a MASH TL-3 thrie-beam roadside system for protecting errant motorists from a fixed object
2019-39-LSRB

## Slide 28: Design and Testing of a Thrie-beam System at a Fixed Object
Project Background
  WSDOT system for a nested thrie-beam with reduced post spacing shields fixed objects
  Fixed object is in close proximity to roadway need for minimal deflection
  Could provide a cost effective alternative to a concrete barrier
Proposed Work Plan
  Task 1: Design Development
    Review previous literature and research
    Preliminary analysis
    Computer simulation
  Task 2: MASH Crash Testing
    Crash test the roadside system to MASH TL-3.
2019-39-LSRB

## Slide 29: Design and Testing of a Thrie-beam System at a Fixed Object
Deliverables
  Design for a MASH compliant roadside thrie-beam barrier that provides a “close to rigid” condition
  Technical report documenting the project
Urgency and Expected Benefit
  Provides a cost effective alternative to concrete barriers when minimal deflection is needed
Funding
  $
Research Period
  months
2019-39-LSRB

## Slide 30: 31” W-beam Guardrail (Steel and Wood Post) in Asphalt Mow Strips
PS Developers Kurt Brauner, LA
Project Synopsis
  There is a need to install the W-beam guardrail system in asphalt without having to construct a concrete mow-strip to control vegetation. Currently there is no design of the mow-strip for asphalt
Project Goal(s)
To develop and test an asphalt mow-strip that allows installation of wood post and steel post W-beam guardrails with posts installed directly in asphalt as opposed to a backfilled low-strength grout. Testing would be needed for MASH TL-3 for both systems
2019-40-LSRB
Project Background
  Need MASH system for installing the wood & steel post guardrail in asphalt, without a concrete mow-strip
  Previous MASH Tests 3-10 and 3-11 were successful on steel post W-beam guardrail in concrete mow strip
  This design was unsuccessful for wood-post W-beam. It passed MASH Test 3-10, but failed Test 3-11

## Slide 31: 31” Rectangular Wood Post W-Beam Guardrail in Concrete Mow Strips
Proposed Work Plan
Task 1: Bogie Testing
  Perform impact tests of posts installed in various thicknesses of asphalt and compare the force deflection behavior to posts directly installed in soil
  Select designs for the full-scale system
  Testing to be performed for both wood and steel posts
Task 2: Construction
  Construct and repair test installations of wood-post W-beam guardrail and steel post W-beam guardrail
Task 3: Testing and Reporting
  Perform MASH Test 3-10 and Test 3-11 for both steel post and wood post guardrail systems
  Prepare final report
Deliverables
Final report
Engineering drawings
2019-40-LSRB

## Slide 32: 31” Rectangular Wood Post W-Beam Guardrail in Concrete Mow Strips
Urgency and Expected Benefit
Successful designs will allow agencies to install the W-beam guardrail system in asphalt without having to construct a concrete mow-strip to control vegetation. Currently there is no design of the mow-strip for asphalt. If successful, this design will see immediate implementation
Funding
Task 1 – Bogie Testing $45,000
Task 2 – Construction $55,000 (2 installations, 2 repairs)
Task 3 – Testing and Reporting
Test 3-10 x 2 $80,000
Test 3-11 x 2 $90,000
TOTAL $251,000
Research Period
12 months
2019-40-LSRB