## Slide 1: BIB Terminal Variations in Foreslope/Backslope/Ditch Configurations
PS Developers: Jeff (AK); Christopher (OR), Josh (CO), Fil (IL)
Project Synopsis
  Evaluate range of BIB ditch configurations (site variations from crash tested conditions), producing acceptable results under MASH conditions.
Project Goal(s)
Consider variations from crash tested configuration to establish acceptable design alternatives, for varying ditch configurations, including:
• BIB terminal may be installed on foreslope flatter than 4:1;
• Flattest effective backslope; investigate whether there is a limit for backslope steepness;
• BIB terminal may be installed in flat-bottomed ditches;
2019-17-LSRB
Project Background
  MASH crash test: 4:1 Foreslope/ 2:1 Backslope/ V-Ditch, TTI project 608431, tests 3-34, 3-35
Notes: Flattest effective backslope; a threshold backslope for requiring area free of fixed objects behind the terminal; and investigate whether there is a limit for backslope steepness.
Ditch configurations vary: the foreslope is flatter than 4:1; foreslope of the ditch is wider than 6 feet; the backslope varies from 2:1; or the ditch is flat-bottomed

## Slide 2
Proposed Work Plan
Task 1. DOT Members Survey.
Identify common applicable ranges with respect to research parameters in use (and needed) by DOT Members (degree of backslope, type of ditch configuration, ditch width, rubrail /no rubrail)
Task 2. Engineering Analysis and Finite Element Investigation.
Conduct engineering analysis to identify most critical cases based on Task 1 results.
Conduct FE computer simulations to investigate critical cases for system crashworthiness.
Task 3. Recommendations.
Summarize recommendations based on engineering analysis (and FEA).
Deliverables
Acceptable limits for foreslope (flatter than 4:1), and backslope (range of variation from 2:1 and critical slope), offset to ditch bottom or width of foreslope, and width of flat-bottomed ditch.
Necessary changes to design for variations
BIB Terminal Variations in Foreslope/Backslope/Ditch Configurations
2019-17-LSRB

## Slide 3: BIB Terminal Variations in Foreslope/Backslope/Ditch Configurations
Urgency and Expected Benefit
BIB Terminal eliminates potential for guardrail terminal end strike. If acceptable limits for slopes or other ditch variability can be shown, more opportunities for BIB installation can reduce risk to the traveling public. A robust MASH BIB is available; it is important to understand the adaptability of the BIB.
State design standards for ditches vary. Demonstrating BIB is adaptable to variation in slopes and ditch design will increase the number of locations this device could be installed.
Funding: $85,620
Research Period : 1 year
2019-17-LSRB