## Slide 1: Determine MASH Compliance of Placing Guide Rail in Rock
PS Developers PF Tech. Rep. TBA (Presenting: Nauman Sheikh, TTI)
Project Synopsis
  Update the current RDG guideline for guardrail post installation in rock using the MASH testing criteria
Project Goal(s)
Update current guardrail in rock guidance using recent and new MASH crash testing.
2020-02-LSRB
Project Background
  Current RDG guidance for guardrail post installation in rock is based on NCHRP Report 350 testing
  Testing was performed with steel post guardrail
  Slightly larger holes were recommended for wood post guardrail
  MASH evaluation/update of the guideline is needed
20”
8”
20”
22.8”
22.8”
9.8”

## Slide 2: Determine MASH Compliance of Placing Guide Rail in Rock
2020-02-LSRB
Project Background
  TTI/TxDOT tested round wood post in rock with oval and round holes – both failed MASH
  TTI/TxDOT tested steel post guardrail in larger oval holes – passed MASH
  Contractors seem to prefer a single round hole over coring two holes to make oval
  If slightly larger hole is acceptable, the steel post system doesn't need to be tested for MASH
  Evaluation and test is needed for rectangular wood post in rock using MASH criteria

## Slide 3: Determine MASH Compliance of Placing Guide Rail in Rock
Proposed Work Plan
Task 1: Past Testing Review & Wood Post System Design
  Evaluate past testing to develop design for the rectangular wood post guardrail in simulated rock
  Get concept design approved from Tech. Rep. prior to testing
Task 2: Construction
  Construct wood-post guardrail in simulated concrete rock for testing
Task 3: Crash Testing, Guideline, & Final Report
  Perform MASH Test 3-10 and 3-11
  Use results of the new and past testing to recommend update to guideline
  Final Report
Deliverables
Final report including the guideline and system drawings
2020-02-LSRB

## Slide 4: Determine MASH Compliance of Placing Guide Rail in Rock
Urgency and Expected Benefit
Wood post guardrail is widely used and when rock is encountered, a MASH compliant guidance is needed for proper installation.
The guidance will be a recommended update to the RDG’s current guidance for both steel and wood post systems
Funding
Total Cost Estimate = $145,503
  Task 1 - $13,218
  Task 2 - $45,957 (includes repairs for retesting and demolition & disposal after project)
  Task 3 - $86,328 (Test 3-11 and Test 3-10)
Research Period
12 months
2020-02-LSRB