## Slide 1: Desing and Testing of New Anchored PCB System
Supplemental Project - Caltrans
By
Nauman Sheikh, P.E. (TTI)
Bob Meline, P.E. (Caltrans)

## Slide 2: Background
Caltrans NJ profile restrained Type-K PCB does not meet MASH TL-3 criteria
  Desire to change over to F-shape profile
  Use Oregon/TTI connection and barrier detail because of its history of good performance and low deflections in testing
Current TTI/Pooled Fund F-shape PCB uses inclined pins, which are less desirable for installation in asphalt
Caltrans wanted to use vertical pins

## Slide 3: Research Objectives
Develop an F-shape PCB system using the Oregon/TTI barrier design that can be use as:
  Roadside barrier - anchored on asphalt
  Median barrier - anchored on asphalt
  Roadside barrier - anchored on concrete
  Median barrier - anchored on concrete with shallower anchor bolts (can also be a roadside barrier)
Several barrier design features were needed
  Reinforced segment toe areas
  Strengthened anchor pin/bolt holes
  Lifting holes
  Drainage scuppers

## Slide 4: Research Approach
Developed barrier design details
Developed FE model of the barrier system and performed impact simulations
Refined the design
Constructed test installations
Performed four MASH Test 3-11, one for each configuration

## Slide 5: Barrier Details
12-ft F-shape
Pin-and-loop connections (same as Oregon/TTI design)
Lifting sleeves
3” tall drainage scuppers
3 holes for anchor pins/bolts on each side

## Slide 6: Barrier Details
Toe reinforcement (C-bar)
Anchor bolt/pin slot reinforcement (Z-bar and slotted plate)
Lifting holes

## Slide 7: Barrier Details
Reinforcement details

## Slide 8: Simulation Analysis
Barrier Segment Model

## Slide 9: Simulation Analysis
Anchored on Asphalt, Roadside Configuration, Pins on Impact Side

## Slide 10: Simulation Analysis
Anchored on Asphalt, Roadside Configuration, Pins on Impact Side

## Slide 11: Simulation Analysis
Anchored on Asphalt, Roadside Configuration, Pins on Impact Side
*Video Removed for size*

## Slide 12: Simulation Analysis
Anchored on Asphalt, Roadside Configuration, Pins on Impact Side
Barrier Damage & Deflection

## Slide 13: Simulation Analysis
Anchored on Asphalt, Roadside Configuration, Pins on Impact Side
Barrier Damage & Deflection
 | Test 3-11 | Test 3-10
Permanent Deflection (in) | 6 | 1.8
Max. Dynamic Deflection (in) | 8.1 | 4.4
Overhang from Pavement Edge (in) | None | None

## Slide 14: Simulation Analysis
Simulation analyses were performed for other configurations
  Anchored on Asphalt, Roadside Configuration, 3 Pins on Impact Side
    Simulation of Test 3-11
    Simulation of Test 3-10
  Anchored on Asphalt, Median Configuration, 4 pins (1 on each corner)
    Simulation of Test 3-11
  Anchored on Concrete with epoxy anchor constraints on impact side
    Simulation of Test 3-11
All simulation results indicated design would pass MASH
Full-scale crash testing was recommeded

## Slide 15: Crash Testing
Pinned to Asphalt as Roadside Barrier
Pinned on traffic side only
3 pins per 12-ft segment
36-inch long pins
4-inch thick asphalt
6-inch offset from vertical cut

## Slide 16: Crash Testing
Pinned to Asphalt as Roadside Barrier

## Slide 17: Crash Testing
Pinned to Asphalt as Roadside Barrier
*video removed for size*

## Slide 18: Crash Testing
Pinned to Asphalt as Roadside Barrier
*Video removed for size*

## Slide 19: Crash Testing
Pinned to Asphalt as Roadside Barrier
TEST ARTICLE DEFLECTIONS | 
Dynamic (inches) | 10.1
Permanent (inches) | 5
Working Width / Height (inches) | 30.5 / 59.6

## Slide 20: Crash Testing
Pinned to Asphalt as Median Barrier
Pinned on both sides
4 pins per 12-ft segment
  1 each corner
36-inch long pins
4-inch thick asphalt

## Slide 21: Crash Testing
Pinned to Asphalt as Median Barrier
*video removed for size*

## Slide 22: Crash Testing
Pinned to Asphalt as Median Barrier
*video removed for size*

## Slide 23: Crash Testing
Pinned to Asphalt as Median Barrier
TEST ARTICLE DEFLECTIONS | 
Dynamic (inches) | 7.2
Permanent (inches) | 0.75
Working Width / Height (inches) | 30.3 / 67.3

## Slide 24: Crash Testing
Pinned to Concrete as Roadside Barrier
Epoxy anchor bolts on traffic side
3 anchors bolts per 12-ft segment
6-inch anchor embedment
6-inch offset from edge

## Slide 25: Crash Testing
Pinned to Concrete as Roadside Barrier
*video removed for size*

## Slide 26: Crash Testing
Pinned to Concrete as Roadside Barrier
*video removed for size*

## Slide 27: Crash Testing
Pinned to Concrete as Roadside Barrier
TEST ARTICLE DEFLECTIONS | 
Dynamic (inches) | 3.9
Permanent (inches) | 2.5
Working Width / Height (inches) | 27.6 / 3.0

## Slide 28: Crash Testing
Pinned to Concrete with Reduced Anchor Embedment (Roadside or Median)
Epoxy anchor bolts four corner
4 anchors bolts per 12-ft segment
5-inch anchor embedment
6-inch offset from edge

## Slide 29: Crash Testing
Pinned to Concrete with Reduced Anchor Embedment (Roadside or Median)
*video removed for size*

## Slide 30: Crash Testing
Pinned to Concrete with Reduced Anchor Embedment (Roadside or Median)
*video removed for size*

## Slide 31: Crash Testing
Pinned to Concrete with Reduced Anchor Embedment (Roadside or Median)
TEST ARTICLE DEFLECTIONS | 
Dynamic (inches) | 10.1
Permanent (inches) | 5
Working Width / Height (inches) | 30.5 / 59.6

## Slide 32: Conclusions
All four MASH Test 3-11 passed
The new PCB system is ready for use as:
  Median barrier on asphalt and concrete
  Roadside barrier on asphalt and concrete
Caltrans intends to do further research in developing transitions to rigid and free-standing barrier
  Looking for collaborating states
 | Max. Dynamic Deflection (in) | Permanent Deflection (in)
On asphalt as roadside barrier | 10.1 | 5.0
On asphalt as median barrier | 7.2 | 0.75
On concrete as roadside barrier | 3.9 | 2.5
On concrete with reduced anchor embedment | 10.1 | 5.0